## Slide 1: Big Bay Dam Failure Analysis using DLBreach and WinDAM
Mitchell L. Neilsen
Department of Computer Science
Kansas State University, Manhattan, KS
United States Department of Agriculture
Agricultural Research Service
Natural Resources Conservation Service
Notes: This project involves the development of simulation environment that can be used to evaluate vegetated earth and rock spillways at the watershed scale. Key variables can be specified using probabilistic distributions, and samples for those variables can be generated using either Monte Carlo or Latin Hypercube Sampling. LHS requires fewer samples to achieve the same level of precision.
This project involves a collaborative research effort between KSU, the USDA, and the US Army Corps of Engineers. Spillway erosion is simulated using a three phase erosion model. The first phase is vegetal cover failure, the second phase is concentrated flow erosion, and the third phase is headcut advance. The focus of this paper is on the software architecture. Other recent papers focus on the model and the theoretical basis for the model.

## Slide 2: Windows* Dam Analysis Modules (WinDAM)
WinDAM is a modular framework for the design and analysis of water control structures (dams).
WinDAM A
WinDAM B
Reservoir Routing Module with Dam Overtopping
SITES Spillway Erosion Analysis with Latin Hypercube Sampling
Dam Breach Analysis Module
Embankment Erosion Module
Internal Erosion Module
Zoned Embankment Erosion Module
WinDAM A+
WinDAM C
WinDAM D
HEC-RAS
WinTR-20
SITES
Notes: This paper describes the software components included in the integrated development environment, and a description of the flow of control and data through the environment. The software consists of four different componets, SitesSim is a module derived from Sites to compute the amount of erosion that occurs, an Integrity Checker to verify the syntactic correctness of the input data -- logical correctness is still up to the designer, although some warnings will be generated if some input parameters appear to be out of the normal range, DakotaLHS generates random samples based on the distribution specified by the user for a given variable, and finally the master application that controls overall data and control flow, interaction with the user, and parsing of input and output files to make them meaningful to the various components is the IDE SSEA.exe.

## Slide 3: WinDAM Computational Model
Computational Model (WinDAM)
Probability distribution
defining material properties
Random values
for material properties
Latin Hypercube Sampling (Dakota)
WinDAM User Interface

## Slide 4: Flip the Paradigm: Use Dakota to Drive the Analysis
Dakota User Interface
Computational Model (WinDAM C or DLBreach)

## Slide 6: DLBreach Template
Initial_Piping_Breach 17.4, {pw} ! 0.01 to 0.05

## Slide 7: DLBreach
Cohesive_Soil_Erosion_kd {kd} ! 1.5 to 66

## Slide 8: Dam Storage
Chart: Storage description
| 0 | 17.5 | 26.36
 | 71.9 | 84.7 | 86.1
option 2 | 71.9 | 84.73 | 84.89 | 86.1
Option 3 | 71.9 | 84.89

## Slide 9: DLBreach
Upstream_Reservoir 0, 4
0 0
12.83 {uv}
12.99 17500000
14.2 26360000

## Slide 10: Dakota Driver
DLBreachRun.in

## Slide 11
Dakota INTERFACE – analysis DRIVER

## Slide 12
params.in
results.out

## Slide 13: Dakota ANALYSIS Driver
DLBreach.bat
perl dprepro params.in BigBay_cards_template.txt BigBay_cards.txt
-- insert parameters in template and output BigBay_cards.txt
echo "BigBay_cards" | DLBreach_Barrier.exe
-- invoke DLBreach_Barrier.exe to simulate run
python parseOut.py BigBay_cards.out results.out
-- extract results of interest

## Slide 14
Max discharge, max top width, time

## Slide 15
Chart: Max Q vs kd
| 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66
q | 770.5743 | 4358.7685 | 6021.2368 | 770.5631 | 4357.6611 | 6020.291 | 770.5582 | 4357.1768 | 6020.169 | 770.5743 | 3881.655 | 5359.3535 | 770.5631 | 3880.4165 | 5359.0527 | 770.5582 | 3880.5962 | 5358.9541 | 770.5743 | 3336.6162 | 4613.9307 | 770.5631 | 3336.6926 | 4614.0205 | 770.5582 | 3336.6743 | 4613.9424
Observed max discharge 4200 cms

## Slide 16
Chart: Max top width vs kd
| 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66
w | 40.9904 | 160.5395 | 223.5749 | 41.0321 | 160.5453 | 223.5781 | 41.0511 | 160.5475 | 223.5789 | 41.0714 | 165.1712 | 230.7971 | 41.1219 | 165.177 | 230.8002 | 41.1443 | 165.1793 | 230.8011 | 41.13 | 169.4671 | 237.7307 | 41.1905 | 169.4756 | 237.7354 | 41.2167 | 169.4791 | 237.7369
Observed max top width 96 m

## Slide 17
Chart: Max Q time vs kd
| 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66
t | 2.3721 | 1.0055 | 0.71382 | 1.8249 | 0.98049 | 0.70132 | 1.5777 | 0.96938 | 0.69576 | 2.3721 | 0.8916 | 0.63187 | 1.8249 | 0.86799 | 0.61937 | 1.5777 | 0.85688 | 0.61382 | 2.3721 | 0.79576 | 0.56937 | 1.8249 | 0.77076 | 0.55687 | 1.5777 | 0.76104 | 0.55132
Observed max discharge time 0.9167 hr

## Slide 18
Chart: Max Q vs pipe width (pw)
| 0.01 | 0.01 | 0.01 | 0.03 | 0.03 | 0.03 | 0.05 | 0.05 | 0.05 | 0.01 | 0.01 | 0.01 | 0.03 | 0.03 | 0.03 | 0.05 | 0.05 | 0.05 | 0.01 | 0.01 | 0.01 | 0.03 | 0.03 | 0.03 | 0.05 | 0.05 | 0.05
q | 770.5743 | 4358.7685 | 6021.2368 | 770.5631 | 4357.6611 | 6020.291 | 770.5582 | 4357.1768 | 6020.169 | 770.5743 | 3881.655 | 5359.3535 | 770.5631 | 3880.4165 | 5359.0527 | 770.5582 | 3880.5962 | 5358.9541 | 770.5743 | 3336.6162 | 4613.9307 | 770.5631 | 3336.6926 | 4614.0205 | 770.5582 | 3336.6743 | 4613.9424
Observed max Q
4200 cms

## Slide 19
Chart: Max Q vs uv
| 13870000 | 13870000 | 13870000 | 13870000 | 13870000 | 13870000 | 13870000 | 13870000 | 13870000 | 15577224.800000001 | 15577224.800000001 | 15577224.800000001 | 15577224.800000001 | 15577224.800000001 | 15577224.800000001 | 15577224.800000001 | 15577224.800000001 | 15577224.800000001 | 17284449.600000001 | 17284449.600000001 | 17284449.600000001 | 17284449.600000001 | 17284449.600000001 | 17284449.600000001 | 17284449.600000001 | 17284449.600000001 | 17284449.600000001
q | 770.5743 | 4358.7685 | 6021.2368 | 770.5631 | 4357.6611 | 6020.291 | 770.5582 | 4357.1768 | 6020.169 | 770.5743 | 3881.655 | 5359.3535 | 770.5631 | 3880.4165 | 5359.0527 | 770.5582 | 3880.5962 | 5358.9541 | 770.5743 | 3336.6162 | 4613.9307 | 770.5631 | 3336.6926 | 4614.0205 | 770.5582 | 3336.6743 | 4613.9424
Observed max discharge 4200 cms

## Slide 20
Chart: Max width vs Max Q
| 770.57434000000001 | 4358.7685499999998 | 6021.2368200000001 | 770.56311000000005 | 4357.6611300000004 | 6020.2910199999997 | 770.55822999999998 | 4357.1767600000003 | 6020.1689500000002 | 770.57434000000001 | 3881.6550299999999 | 5359.3535199999997 | 770.56311000000005 | 3880.4164999999998 | 5359.0527300000003 | 770.55822999999998 | 3880.5961900000002 | 5358.9540999999999 | 770.57434000000001 | 3336.6162100000001 | 4613.93066 | 770.56311000000005 | 3336.69263 | 4614.0205100000003 | 770.55822999999998 | 3336.6743200000001 | 4613.9423800000004
w | 40.9904 | 160.5395 | 223.5749 | 41.0321 | 160.5453 | 223.5781 | 41.0511 | 160.5475 | 223.5789 | 41.0714 | 165.1712 | 230.7971 | 41.1219 | 165.177 | 230.8002 | 41.1443 | 165.1793 | 230.8011 | 41.13 | 169.4671 | 237.7307 | 41.1905 | 169.4756 | 237.7354 | 41.2167 | 169.4791 | 237.7369

## Slide 21: WinDAM C Analysis
Dakota User Interface
Computational Model (WinDAM C or DLBreach)

## Slide 22: WinDAM Template (BigBay.WDT)
WINDAM 10/06/2022IE Models Eval - BigBay
OPTION SIMPLE BARESOIL NOPS INTERNAL
IEMODEL 2 120.0 {kd } 100 0.002
HYD 0.1 0 0C
..
0
ENDTABLE
CRESTPRFL
0 57.0866
1968.5 57.0866
ENDTABLE
STROUTE 44.29 0 ELEV
STRUCTURE BigBay
0 0
42.09 {uv}
42.62 14187.5
46.59 21370.4
ENDTABLE
UPSTREAM 3 0.016
DAMCREST 40 0.016
DWNSTREAM 3 0.016
CONDUIT {pw } {pw } 2 984.25
TAILWATER
ENDTABLE
OUTPUT ALL
ENDRUN

## Slide 23: WinDAM C Interface

## Slide 24: WinDAM C Analysis
Dakota User Interface
Computational Model (WinDAM C or DLBreach)

## Slide 25: DAKOTA Analysis Driver – WinDAM.bat
parseIn
params.in
newParams.in

## Slide 26: DAKOTA Analysis Driver
Example2.WDT
example.WDC
dprepro

## Slide 27: WinDAM C Analysis
Dakota User Interface
Computational Model (WinDAM C or DLBreach)

## Slide 28: DAKOTA Analysis Driver
WinDamSim
BigBay.WDC
BigBay.OUT

## Slide 29: WinDAM C Analysis
Dakota User Interface
Computational Model (WinDAM C or DLBreach)

## Slide 30: DAKOTA Analysis DriveR

## Slide 31: WinDAM C Analysis
Dakota User Interface
Computational Model (WinDAM C or DLBreach)

## Slide 33
Chart: Max Q vs kd
Observed max Q
4200 cms

## Slide 34
Chart: Max Q vs Pipe Width (pw)
Observed max Q
4200 cms

## Slide 35
Chart: Max top width vs kd
| 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66
w | 40.9904 | 160.5395 | 223.5749 | 41.0321 | 160.5453 | 223.5781 | 41.0511 | 160.5475 | 223.5789 | 41.0714 | 165.1712 | 230.7971 | 41.1219 | 165.177 | 230.8002 | 41.1443 | 165.1793 | 230.8011 | 41.13 | 169.4671 | 237.7307 | 41.1905 | 169.4756 | 237.7354 | 41.2167 | 169.4791 | 237.7369
Observed max top width 96 m

## Slide 36
Chart: Max Q time vs kd
| 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66 | 1.5 | 33.75 | 66
t | 2.3721 | 1.0055 | 0.71382 | 1.8249 | 0.98049 | 0.70132 | 1.5777 | 0.96938 | 0.69576 | 2.3721 | 0.8916 | 0.63187 | 1.8249 | 0.86799 | 0.61937 | 1.5777 | 0.85688 | 0.61382 | 2.3721 | 0.79576 | 0.56937 | 1.8249 | 0.77076 | 0.55687 | 1.5777 | 0.76104 | 0.55132
Obs. max discharge time 0.9167 hr

## Slide 37
Chart: Max width vs Max Q
| 770.57434000000001 | 4358.7685499999998 | 6021.2368200000001 | 770.56311000000005 | 4357.6611300000004 | 6020.2910199999997 | 770.55822999999998 | 4357.1767600000003 | 6020.1689500000002 | 770.57434000000001 | 3881.6550299999999 | 5359.3535199999997 | 770.56311000000005 | 3880.4164999999998 | 5359.0527300000003 | 770.55822999999998 | 3880.5961900000002 | 5358.9540999999999 | 770.57434000000001 | 3336.6162100000001 | 4613.93066 | 770.56311000000005 | 3336.69263 | 4614.0205100000003 | 770.55822999999998 | 3336.6743200000001 | 4613.9423800000004
w | 40.9904 | 160.5395 | 223.5749 | 41.0321 | 160.5453 | 223.5781 | 41.0511 | 160.5475 | 223.5789 | 41.0714 | 165.1712 | 230.7971 | 41.1219 | 165.177 | 230.8002 | 41.1443 | 165.1793 | 230.8011 | 41.13 | 169.4671 | 237.7307 | 41.1905 | 169.4756 | 237.7354 | 41.2167 | 169.4791 | 237.7369

## Slide 38
Chart: Max Q vs uv
Observed max Q
4200 cms

## Slide 39
Chart: Max time (hr) vs Max Q (cms)
Observed max Q
4200 cms
Obs. max discharge time 0.9167 hr