## Slide 1: Sensitivity Analysis of Internal Erosion Models for Dam Safety
Mitchell Neilsen, Chendi Cao
Department of Computer Science
Kansas State University Manhattan, KS, USA
{ neilsen@ksu.edu, caocd@ksu.edu }
Notes: This project involves the development of simulation environment that can be used to evaluate vegetated earth and rock spillways at the watershed scale. Key variables can be specified using probabilistic distributions, and samples for those variables can be generated using either Monte Carlo or Latin Hypercube Sampling. LHS requires fewer samples to achieve the same level of precision.
This project involves a collaborative research effort between KSU, the USDA, and the US Army Corps of Engineers. Spillway erosion is simulated using a three phase erosion model. The first phase is vegetal cover failure, the second phase is concentrated flow erosion, and the third phase is headcut advance. The focus of this paper is on the software architecture. Other recent papers focus on the model and the theoretical basis for the model.

## Slide 2: Tuttle Creek Reservoir Dam
Dam
Principal Spillway
Auxiliary
Spillway
Kansas
State
University

## Slide 3: Auxiliary Spillway Discharge (1993)
Peak Flow: 60,000 cfs = 1,700 cms
Duration: 21 days
Notes: 18

## Slide 4: Spillway After 1993 Flood
Scarp Heights
up to 24 ft. (7 m.)
Erosion: 400,000 yd3
307,000 m3
Auxiliary Spillway Erosion (1993)
Notes: 20

## Slide 5: Example: Tuttle Creek Spillway

## Slide 6: Example: Tuttle Creek Spillway
Actual Erosion

## Slide 7: Causes of Dam Failures
Causes of Dam Failures* Percentage
Dam overtopping and auxiliary spillway failure 23 – 52%
Piping/seepage/internal erosion 25 – 44%
Slides 2 – 15%
Miscellaneous 9 – 40%
* V. Singh, “Dam breach modeling technology”, 1993.

## Slide 8: Windows* Dam Analysis Modules (WinDAM)
WinDAM is a modular framework for the design and analysis of water control structures (dams).
A+
B
C
D
Notes: This paper describes the software components included in the integrated development environment, and a description of the flow of control and data through the environment. The software consists of four different componets, SitesSim is a module derived from Sites to compute the amount of erosion that occurs, an Integrity Checker to verify the syntactic correctness of the input data -- logical correctness is still up to the designer, although some warnings will be generated if some input parameters appear to be out of the normal range, DakotaLHS generates random samples based on the distribution specified by the user for a given variable, and finally the master application that controls overall data and control flow, interaction with the user, and parsing of input and output files to make them meaningful to the various components is the IDE SSEA.exe.

## Slide 9: Weir Upstream of Test Embankment USDA Hydraulic Engineering Research Unit (HERU)

## Slide 10: Dam Overtopping Breach Analysis

## Slide 11: Dam Overtopping Breach Analysis

## Slide 12: Internal Erosion Analysis (weak silty sand material - SM)
e) 13 min., f) 60 minutes.

## Slide 13: t >> tc Rapid Internal Erosion
OK ARS HERU
kd ~ 57 (ft/hr)/psf
tc ~ 0 psf

## Slide 14: WinDAM Headcut Model Input
Silty sand (SM) material properties

## Slide 15: Internal Erosion Analysis (stronger clay material - CL)
e) 46 hours f) 72 hours.

## Slide 16: t ~ tc Negligble Internal Erosion
OK ARS HERU
kd ~ 0.017 (ft/hr)/psf
tc ~ 0.0 psf

## Slide 17: WinDAM Headcut Model Input
Clay (CL) material properties

## Slide 18: JET Field test for kd
Submerged jet from known orifice diameter
Measured height above bare soil
Erosion is measured over time kd

## Slide 19: JET Lab Samples
ARS HERU
Notes: This slide shows how the different samples responded to the laboratory jet erosion test.

## Slide 21: WinDAM Computational Model
Compute hydrodynamics (WinDamSim)
Post-processing: Extract hydrograph(s) (WinDAM)
Pre-processing: Generate mesh and dam model (WinDAM)
Compute dam or spillway erosion (SitesSim)

## Slide 22: Internal Erosion Flow Conditions

## Slide 23: WinDAM Output

## Slide 24: Using DAKOTA to drive the Analysis
Analysis Model (DAKOTA)
Pre-processing: Input Parameters
Post-processing: Response Metrics
Computational Model (WinDamSim or SitesSim)
WinDAM User Interface
DAKOTA User Interface

## Slide 25: DAKOTA
DAKOTA: Design and Analysis tooKit for Optimization and Terascale Applications - by Sandia National Laboratories
DAKOTA adds value to simulation-based analysis:
  Sensitivity - which input parameters affect performance metrics?
  Uncertainty (quantification) - how safe, reliable, robust or variable is the system?
  Optimization - which design performs best?
  Calibration - which models and parameters best match empirical data?
  Parameter studies - vary input, how does output change?
All require iterative analysis with the computational model.

## Slide 26: DAKOTA User Interface (for parameter studies)
…
…
Tw
Kd
…
…
Tw
Kd

## Slide 27: DAKOTA Input File

## Slide 28: Using DAKOTA to drive the Analysis
Analysis Model (DAKOTA)
Pre-processing: Input Parameters
Post-processing: Response Metrics
Computational Model (WinDamSim)
WinDAM User Interface
DAKOTA User Interface

## Slide 29: Using DAKOTA to drive the Analysis
Analysis Model (DAKOTA)
Pre-processing: Input Parameters
Post-processing: Response Metrics
Computational Model (WinDamSim)
WinDAM User Interface
DAKOTA User Interface

## Slide 30: DAKOTA Analysis Driver (WinDam.bat)
2 variables
0108.0000 Tw
0000.0170 Kd
parseWinDamIn
params.in
newParams.in

## Slide 31: DAKOTA Analysis Driver (WinDam.bat)
dprepro
example.WDT
example.WDC

## Slide 32: Using DAKOTA to drive the Analysis
Analysis Model (DAKOTA)
Pre-processing: Input Parameters
Post-processing: Response Metrics
Computational Model (WinDamSim)
WinDAM User Interface
DAKOTA User Interface

## Slide 33: DAKOTA Analysis Driver (WinDam.bat)

## Slide 34: Using DAKOTA to drive the Analysis
Analysis Model (DAKOTA)
Pre-processing: Input Parameters
Post-processing: Response Metrics
Computational Model (WinDamSim)
WinDAM User Interface
DAKOTA User Interface

## Slide 35: Dakota 6.10 Input Format

## Slide 36: Centered Parameter Study Results

## Slide 38: Resulting Sobel Indices

## Slide 40: Summary
WinDAM
  Provides a framework to combine existing models and develop new models for dam erosion analysis
Dakota
  Provides a framework for parameters studies, uncertainty quantification, and sensitivity analysis
Together, they provide a powerful framework for dam safety analysis

## Slide 41: http://www.damsafety.info

## Slide 42: Next Steps
International Internal Erosion Breach Model Performance Evaluation
  EMBREA – HR Wallingford (www.dambreach.org)
  WinDAM – USDA, KSU (www.damsafety.info)
  AREBA – EDF
  DL BREACH – Clarkson University
  RUPRO – IRSTEA

## Slide 43: Next Steps

## Slide 44: Questions?